## Slide 1: WiFi Sniffer w/RaspberryPi
yintao_ling

## Slide 2: RaspberryPi Connection
Console：
  SSH
File：
  FTP
GUI：
  VNC Server (Not supported Wireshark)
  RDP Server

## Slide 3: RaspberryPi Connection
172.16.0.49
ssh://172.16.0.49
ftp://172.16.0.49
vnc://172.16.0.49:5901
rdp://172.16.0.49 (One user only for free license. Wireshark Available.)

## Slide 4: RaspberryPi Setup
yintao_ling

## Slide 5: RaspberryPi Setup - VNC Server
Tightvncserver
Modified ~/.vnc/xstartup for Kali & Windows 10
Auto start script in /etc/init.d/vncserver (rc.d)
Auto start script in /etc/systemd/system/vncserver@.service
Auto start by crontab
  @reboot su - kali -c ‘/usr/bin/vncserver :1 -geometry 1024x768’

## Slide 6: RaspberryPi Setup
Port 5901 - VNC Server
Port 3389 - RDP Server

## Slide 7: RaspberryPi Setup - VNC Server
Using UltraVNC on Windows.
Address = <IP>::5901

## Slide 8: RaspberryPi Setup - VNC Server

## Slide 9: RaspberryPi Setup - RDP Server
Windows Remote Desktop

## Slide 10: RaspberryPi Setup - RDP Server

## Slide 11: RaspberryPi Setup - RDP Server

## Slide 12: Wireless Commands
yintao_ling

## Slide 13: Wireless commands
ifconfig wlan0 up/down
iwconfig wlan0 essid <NAME> key s:<PASSWORD> (WEP)
/etc/wpa_supplicant.conf (WPA)
dhclient wlan0
nmcli
sudo iwlist wlan0 scan | grep ssid | sort

## Slide 14: 802.11 on Wireshark
yintao_ling

## Slide 15: Wireshark
In normal situations user cannot see 802.11 Frame from Wireshark.
Link-Layer transforms 802.11 packets into fake Ethernet packets.
  Reference from Wireshark Website.

## Slide 16: Wireshark
In order to see 802.11 Frame, Wi-Fi adapter and OS must be in monitor mode.

## Slide 17: Managed Mode
Wireless Interface Info.

## Slide 18: Monitor Mode
Wireless Interface Info.

## Slide 19: Monitor Mode
There are 3 tools to change Wireless interface into monitor mode.
  iw
  iwconfig
  airmon-ng
Remember to disconnect current ESSID.

## Slide 20: iw
Managed Mode to Monitor Mode
  sudo ip link set wlan0 down
  sudo iw wlan0 set monitor mode
  sudo ip link set wlan0 up
Monitor Mode to Managed Mode
  sudo ip link set wlan0 down
  sudo iw wlan0 set type managed
  sudo ip link set wlan0 up

## Slide 21: iwconfig
Managed Mode to Monitor Mode
  sudo ifconfig wlan0 down
  sudo iwconfig wlan0 mode monitor
  sudo ifconfig wlan0 up
Monitor Mode to Managed Mode
  sudo ifconfig wlan0 down
  sudo iwconfig wlan0 mode managed
  sudo ifconfig wlan0 up

## Slide 22: airmon-ng
Check supported interface = sudo airmon-ng
Check related processes = sudo airmon-ng check kill
Close related processes = sudo airmon-ng check kill
sudo airmon-ng start wlan0
sudo airmon-ng stop wlan0mon

## Slide 23: Approach 1 - airmon-ng
yintao_ling

## Slide 24: airmon-ng
sudo airmon-ng start wlan0
  Creating wlan0mon monitor interface over wlan0.

## Slide 25: airmon-ng
Wireshark does detect wlan0mon interface.

## Slide 26: airmon-ng

## Slide 27: airmon-ng
sudo airmon-ng stop wlan0mon
  Restore wlan0 interface into managed mode.

## Slide 28: Conclusion to Approach 1
Feel very unreliable with airmon-ng tool.
Easily to crash on Wireshark.

## Slide 29: Approach 2 - iw
yintao_ling

## Slide 30: Getting started with iw
Checking monitor support on phy#0

## Slide 31: Checking phy0 info

## Slide 32: Checking phy0 info

## Slide 33: Capturing in Monitor Mode
sudo iw phy phy0 interface add mon0 type monitor

## Slide 34: Capturing in Monitor Mode
sudo ifconfig wlan0 down
sudo iw dev mon0 set freq 2437 (Channel 6)
sudo ifconfig mon0 up

## Slide 35: Checking phy0 info

## Slide 36: Checking phy0 info

## Slide 37: Capturing 802.11 Packets

## Slide 38: Restoring to Managed Mode
sudo ifconfig wlan0 up
sudo ifconfig mon0 down

## Slide 39: Conclusion to Approach 2
I think this is the better method rather than Approach 1.
The additional interface is much easier to manage.
However, the memory storage for packets is really large.
Need to re-setup once rebooting. -> Create script file ?

## Slide 40: MacBook Air

## Slide 41: Wireshark Filter for 802.11

## Slide 42: Reference
https://askubuntu.com/questions/120973/how-do-i-start-vnc-server-on-boot
https://askubuntu.com/questions/41273/how-to-copy-paste-text-from-remote-system
https://www.raspberrypi.org/forums/viewtopic.php?t=216725
https://sandilands.info/sgordon/capturing-wifi-in-monitor-mode-with-iw
sudo update-rc.d vncserver defaults
sudo systemctl enable vncserver

## Slide 43: Thank you for listening
yintao_ling